1 Apr. 1990

Tranquillity Catapults, 3 strikes one error,

or does this bus stop at the Mare Imbrium

by

David G. Stephenson

Scouts explored the interior of the New World, and settlers may have traveled by wagon trains, but it was the railroad that made the exploitation of the American frontier possible. Despite the romance of the luxury transcontinental expresses, like any transportation system, anywhere, anytime, the railroads depended on freight to pay the bills, and without doubt the same economic reality will mold the exploitation of the new frontier of space.

There would have been no freight for the great transcontinental trunk lines without a network of local routes fanning out across the American West. Just as the coastal cities of America were dependent on the resources of the interior, so space manufacturing centers will need trade routes to the lunar mining sites. The best system for shipping ores from the Moon into space seems to be the mass driver or electromagnetic catapult, situated somewhere near the equator.

But mass driver installations will only be the Chicagos, and Abilenes for the vast hinterland of the new frontier. Although the mineralization of the Moon is not nearly as diverse as that of our own planet, Murphy's Universal Law leads us to expect that the best lodes of anorthite, will be found far from the equator. The pioneer is a determined individualist who would be uncomfortable in the urban lunar capital with its massive political and administrative infrastructure structure. The Moon will surely scatter its opportunities as widely as the Earth. Investors in the space economy will prudently ensure that a major incident at a mine site did not totally disrupt the ilmenite futures market and will welcome alternative sources of supply. Woven across the Moon from major mass driver ports to the scattered mine sites, tourist centers, observatories and, alas, garrisons will be a web of transportation that will evolve to suit the unique conditions found under the wide lunar sky.

Governing every aspect of life on the Moon will the simple fact, first revealed by the Apollo program, that there is virtually no carbon, nitrogen, or hydrogen in the lunar rocks. Almost every other important element is more or less available, but those three vital elements, which are the basis of our industrial processes, our plastics, our chemical rocket fuels and even life itself, are absent. True, some hydrogen may exist as ice at the poles, or in the rocks that have been bombarded by the solar wind for billions of years. But hydrogen is one of the most awkward elements to keep in a container. As a gas it will leak through the crystal structure of many metals, and as a liquid it is bulky and must be stored at very low temperatures. Almost all of our uses for the three vital elements involve dynamic processes, so with constant recycling looses are inevitable, and indeed rocket fuels by definition are discarded after use. Replacement supplies will have to be shipped in at great expense from the Earth or the Asteroids. Cost effective lunar transport systems will not be able to afford these expensive elements, and moving around on the Moon will be very different from being on Earth.

Vital ore and other bulk cargoes will have to be shipped to distant equatorial catapult ports, situated according to a N.A.S.A. study on the east shore of the Sea of Tranquillity. Mass drivers are fueled by electricity, not chemicals, and only the payload and perhaps a ore container or bucket goes into space. They will be the most economical way not only of delivering lunar ores to the Lagrange points in space but also sending them to the space port from a distant mine. A cleared area covered with a deep layer of lunar dust would be the incoming target zone. Recovering shipments should be straight forward, if a trifle messy. But man's technology continually advances. Since that distant day when, as a primitive ape was using a crude rock to try and pulverize the skull of another, the rock chipped to become man's first crafted tool, there have always been unintended civilian spin-offs from military research. Just as the crude rock was superseded by the club and flint blade, so today's anti-satellite weapons will one day be superseded and like rock become available everywhere at dirt cheap prices. A modern anti-satellite drone is lobbed up in front of an oncoming satellite where it uses sophisticated infra-red sensors and a crown of small rockets to hover in the path of an oncoming target. Once in space it really only a matter of convention that the drone is stationary and the target is moving at 5 miles a second. Shipped to the Moon as military surplus drones will be refurbished and lunar miners as terminal guidance systems for their ore shipments. Fixed to a bucket incoming over the Moon the drone would lock onto an infra-red laser beacon beaming out of the open end of a mass driver, and guide it to a precise insertion. The mass driver will function as an electromagnetic catcher to bring the shipment to a controlled halt. Electromagnetic eddy breaking will not only slow the shipment but also recover the energy originally used to catapult the ore shipment, presumably to be stored in large inertial storage units for later reuse. If catapulting rock around the Moon as the lunar day progresses is an economical way of transmitting electricity across the terminator, the Moon of the future will be a cosmic baseball park. There will be an important difference from the terrestrial game in that if there is a catching error, it will be the fielding side that gets the runs!

Of course small mass drivers could send many things beside raw ore shipments around the Moon. Spare parts, dried foods, assay reports that are too sensitive to be transmitted by satellite, and the latest technical and hard porn literature to while away the long, long lunar nights could just as well go by catapult. If an item could, without damage, be accelerated violently, and sent hurtling through empty space before coming to a jarring stop at its destination, then it could safely be included in a flying bucket. In other words, it could contain anything you would happily consider sending by parcel post.

For more delicate items other vehicles will have to be developed. Courier freight and very important people, such as politicians, generals, real estate and commodity speculators, pop and sports stars, and members of the press will surely travel in space craft similar to the Apollo lunar module. These modules will not skim over the lunar surface, but travel along a high ballistic path. It is much simpler to construct a light craft if all the main thrusts are in one direction, and line of sight radio contact will be possible with the point of departure or destination during most of the flight.

Military vessels on the other hand are not concerned with economics and want to stay undetected so they will hug the lie of the land perched on suspensor rockets. Of course rockets need fuel and oxygen. Oxygen may be plentiful, but in place of hydrocarbons lunar rockets will have to burn aluminum metal, which is already the major ingredient in today's solid rockets. But when aluminum burns the result is the familiar white smoke of small alumina spheres seen during a shuttle launch. On Earth these remain out of sight and out of mind as the most common particle in the upper atmosphere. Falling from rocket over the Moon they will descend to the surface as guano trails marking Man's passage across the eternal lunar grayness. No doubt there will be dramatic acts of self-sacrifice to save the pristine face of the Moon performed before the lenses of the media by the 'Friends of the Moon' and 'Greypeace'. Groups universally known as the lunatic fringe of the environmental movement.

The  bad publicity will only be curtailed by the imposition of severe alumina pollution restrictions. Taking off vertically a vehicle will deposit most of its exhaust around the launch pad. Only at a considerable height will the vehicle rotate so that its exhaust will miss the Moon's surface altogether, or by careful throttling join the recyclable mess accumulating around the take off pad.

For the mundane traveler, tourists and other general freight, surface transport will have to suffice. N.A.S.A. designs for the ships of the lunar desert suggest that they may be about the size of municipal buses with sausage-like pressure chambers mounted on a wheeled chassis, and possibly coupled into trains. But such vehicles will need motors and an energy source. Obviously conventional combustion motors are out. Once again there may be plenty of oxygen but it will be expensive and have to be recycled, and there will be no hydrocarbons.

Short range transport near mine site could use batteries and electrical motors like those used by the Apollo lunar rover. After several decades of development terrestrial batteries are still rather bulky and lack the energy capacity needed for long range cross country vehicles. On the Moon batteries must not only supply traction motors, but also lighting, life support systems, communications and computers, perhaps for a fourteen day lunar night.

Maybe staging posts like those of the old west will dot the lunar surface. Here exhausted power cells from an arriving vehicle would have time to recharge their strength before being coupled to another vehicle going in a return direction. Prospectors will want low cost fuels that can be easily cached out on the lunar surface for long periods and fuel cells make electricity from fluid containing oxygen and hydrogen. Liquid oxygen can be stored in large insulated or buried tanks, and as it will be available from the lunar rocks, slow evaporation could be acceptable. Using liquid hydrogen would present severe challenges, and even though the Apollo spacecraft were able to use the waste water coming from their fuel cells, it is unlikely that conventional fuel cells will be used. Instead of hydrogen and oxygen tanks a prospector's cache on the Moon might include a large tank of oxygen rich electrolyte, and a pile of aluminum electrodes. Researchers are currently investigating cells that combine electrolytic oxygen with replaceable aluminum electrodes. Used electrodes could later be returned for recycling at a lunar factory.

Advanced batteries may not be sufficient to power long range, heavy, lunar transports. At least during the daytime it will be possible to tap the ultimate lunar power source, the Sun, to supplement power supplies. There are two ways of doing this, and both are currently being considered for the space station. Arrays of photoelectric semiconducting cells that have powered satellites since the beginning of the space age. They are inefficient but could provide some power to a transport on the Moon.

Solar dynamic generating sets were proposed before the dawn of the space age, and were an intimate part of the famous space stations designed by Von Braun in America or Ross and Smith in Britain in the late l940's and early '50's. A large mirror focuses solar rays onto a boiler that is part of closed cycle heat engine, rather like the toy Sterling cycle engines one can buy from scientific suppliers. In space use the engine would be sealed and contain an organic gas driving a turbine and a high efficiency generator using advanced magnetic materials. There is not going to be much room for solar collectors on a lunar vehicle, so the higher efficiency of solar dynamic power units is going to be attractive, but they also have another advantage. Unlike solar cells, they can use any source of heat at a sufficient temperature.

Chemical reagents are the best way of storing energy in portable form, so alongside the solar boiler could be one designed to burn rather unconventional lunar fuels. Since hydrocarbons are unavailable, the most likely fuels to burn with lunar oxygen will be aluminum or iron. However, aluminum burns at an uncomfortably high temperature, while iron powder burns well in oxygen, and the iron oxide empties can be simply left on the road for the Scouts and Pioneers to collect with a large magnet during their annual recycling 'dust drive'.

Solar collectors would fit on the roofs of vehicles about the size and shape of a familiar city bus. The collector would be a long trough reflector fixed at each end, but able to swing from side to side. A reflector like this would be strong, could be turned upside down for storage, and is very efficient if the Sun is overhead or to one side.

On Earth, modern freight lines are acutely aware that fuel efficiency can be the difference between prosperity and bankruptcy. One airline estimated that if their flight crew each lost 2 kilograms in weight, the company would save several hundred thousand dollars in fuel each year! Clearly the diminutive airhostesses of Singapore Airways have charms that even a flight control computer can appreciate. Some Japanese ship owners are finding that fitting sails to their vessels can save up to 15% of the fuel on a typical voyage.

A lunar bus will be most profitable going north and south at sunrise and sunset, and east or west at noon, but near the equator at noon all directions benefit equally. Lunar buses will proudly bare the image of the hunting dog that can seen on the Full Moon. Route planners for the ‘Poodle Line’ will certainly have these subtleties programmed into their computers, and will not neglect to climb hills in sunlight.

Thanks to the Apollo program we know that the lunar surface is solid and firm and could readily carry serviceable roadways. Although the first prospectors will make their own wandering trails across the Moon, very soon the lunar colonies will be linked by a network of roads marching across the lunar plains like the Roman roads of the barbarian provinces of Gaul and Britannia. And like their Roman prototypes these highways of commerce will be drawn in straight lines with only occasional curves. Roman military engines were large, ponderous and difficult to turn, and lunar trucks will be the same. Tractive force depends upon friction which in turn is proportional to weight, which will be six times less for a given mass, than on Earth. Acceleration, on the other hand, which governs turning and braking, for a given force is proportional to inertial mass, which is the same everywhere. So heavily laden lunar vehicles will respond like railroad trains rather than road vehicles. Acceleration and braking will be gradual, and swerving to avoid an obstruction may have undesirable consequences. As a collision could fatally crack a life support chamber lunar roads will have to be run under strict traffic control, like a railway.

Railroad telegraph lines were replaced by telephones and radios, and now are being superceded by fiber optics cables. On the airless Moon, There will be no need for cables, laser beams will bounce from one colony to another by mirrors or repeaters mounted on poles lined up across the lunar plains. A similar beam lined up along the trade routes could manage traffic and pilot lunar trucks as effectively as a pair of steel rails. Let us hope that tradition is preserved by having the standard gauge of Roman wagons and modern railways of 4 feet 8 1/2 inches continued on the Moon. If communications failed, a stranded traveler would be advised to use the lunar equivalent of a Very pistol. A small radio transmitter shot upwards by some form of emergency mortar would follow a perfect parabola over the lunar surface. Simple radio direction finding systems could pinpoint a crash site within seconds.

Eventually, as the population and trade, increased more sophisticated lunar surface transportation systems will be developed. Futurists may love monorails, but they are simply not competitive with vehicles that travel on two rails. Only one in Germany has been a long-term success. Since the acceleration and turning forces that have to supported by the rail will be as large on the Moon as on Earth, lunar monorails will presumably be just as uncompetitive.

Conventional railways are also unsuitable for the Moon, as you can not make steel rails without carbon. But, iron is available and is the major ingredient in many of the advanced materials that are being developed for the tracks of magnetic levitation railways. Since there is no air resistance on the Moon, a frictionless levi-train could reach high speeds, and once attained, power will only be needed for climbing grades, and possibly braking or switching.

The canals and railways of Earth were both the midwives and children of the industrial revolution. They came into being to transport coal and iron ore to the factories of the world, and grew carrying the products of those factories to market. As they matured they moved all of humanity across the face of the planet. The opening up of space will bring life to the Moon, and future generations will one day look up to see the trains of commerce cris-crossing its ancient face.

David G. Stephenson                      13 Feb. 1986